CCTV SOLUTIONS

The Standard Line

Designed by Mezory, St. Louis, Missouri, USA

www.mezory.com

M I S S I O N  O F  S A F E T Y

MEZORY

MZ-DV

4848i

Mezory 4848i 16 CH REAL-TIME D1 DVR

· Video compression: H.264

· 16 ch video input, 16 ch video output & 16 ch video loops

· 16 ch audio input & 1 ch output

· Display/recording: 480 fps/480fps NTSC,400fps/400fps PAL

· Recording resolution (pixels): 352 x 244 NTSC / 352 x 288 PAL

· Video output: 1 x multiple view BNC, 1 x spot BNC

· HDMI digital output

· 10/100 base network LAN, USB 2.0, VGA, S-video

· IR remote control

· 16 sensor input, 4 alarm output

· Quadplex faster & easier search function for playback retrieval

· 3G built-in smart phone (iPhone iOS, Android … etc)

· SATA II compatible HDD (4 internal SATA HDD up to 2TB & 2 e-SATA

socket for external HDD uo to 2TB HDD storage, maximum of 16TB storage)

· Live, search, backup, PTZ camera controller, remote setup, remote upgrade

· Internal DVR/RW (optional)

· Self-diagnosis and notification of system status with S.M.A.R.T. interface

· MAC client software

MZ-DV-1212i                        MZ-DV-2412i                        MZ-DV-4812i

MEZORY 4CH DVR

· Video compression: H.264

· 4ch video input, 2ch audio input

· Display/recording: 120fps/120fps NTSC, 100fps/100fps

PAL

· Display resolution (pixels): 60/720x480 NTSC,

50/720x576 PAL

· Recording resolution (Pixels): 60/720x480 NTSC,

50/720x576 PAL

· Video output: 2xBNC (multiple view monitor out + spot)

· LAN, 2 USB 2.0 ports, VGA, S-video, IR remote control

· 4 sensors in,1 alarm out

· 3G built-in smart phone (iPhone iOS, Android … etc)

· Multiple network / e-mail alert and FTP upload / MSN

MEZORY 8CH DVR

· Video compression H.264

· 8ch video input, 4ch audio input

· Display/recording 240fps/120fps NTSC, 200fps/100fps

PAL

· Display resolution (pixels): 720x480 NTSC / 720x576PAL

· Recording resolution (pixels): 720x240 NTCS / 720x288

PAL

· Video output: 1BNC (multiple view monitor out + spot)

· LAN, USB 2.0, VGA, S-video

· Alarm, motion detection, video loss, HDD failure

· Smart Phone viewer for iPhone & Android

· Multiple network / e-mail alert and FTP upload / MSN

notification (8ch/16ch)

MEZORY 16CH DVR

· Video compression H.264

· 16ch video input, 4 ch audio input

· Display/recording 480fps/120fps NTSC, 400fps/100fps

PAL

· Display resolution (pixels): 720x480NTSC / 720x576PAL

· Recording resolution (pixels): 360x240NTSC /

360x288PAL

· Video output, 1BNC (multiple view monitor out + spot)

· LAN, 3x USB 2.0, VGA, S-vss, HDD failure

· Smart Phone viewer for iPhone & Android

· Multiple network / e-mail alert and FTP upload / MS

notification (8ch/16ch)

notification (8CH/16CH)

· SATA II compatible HDD (2 internal SATA HDD) & e-

· SATA II compatible HDD (2 internal SATA HDD) & e-SATA

· SATA II compatible HDD (1 internal SATA HDD up to

2TB) & e-SATA for external HDD / 2TB HDD

· Storage: approximately 2000 hours

· DVD/RW backup support

· Video N-streaming

SATA for external HDD / 2TB, ODD (optional)

· HDD storage, approximately 2000 hours

· Faster & easier search function for playback retrieval

· Quadplex faster & easier search function for playback

· MAC client software

w w w . m e z o r y . c o m

for external HDD / 2TB, ODD (optional)

· HDD storage, approximately 2000 hours

· Faster & easier search function for playback retrieval

· Quadplex faster & easier search function for playback

· MAC client software

M I S S I O N  O F  S A F E T Y

MZ-INBP-5694                       MZ-INBD-5604                     MZ-INBZ37H-5604

PIXIM Indoor Box Camera            high-end      Indoor Box Camera                                  Outdoor 37X Optical Zoom Box Camera

· 1/3” PIXIM ORCA sensor, dramatically dynamic range,

Sea wolf DSP Chipset

· Day resolution: 690TVLs ultra high color

· Night resolution: 700TVLs

· Industry-best WDR performance with 120dB max and

95dB standard

· DSS (2~32 fields) and Day/night by digital change

· 4X digital zoom

· Removable IR Cut filter mechanism

· AGC 0~36dB

· Motion detection with 4 active zones

· C/Cs mount

· Minimum illumination: (0.2Lux @ F1.2 50IRE),

(0.0001Lux @ ICR)

· S/N Ratio: more than 53dB

· Built in operational OSD

· 3 axis mirroring and flipping

· 6 privacy zone masking

· 3D motion adoptive DNR

· Synchronization system: internal and external

· 1/3” Sony super HAD IT double density CCD sensor, all

in one A1-DSP chipset

· Day resolution: 600TVLs super high color

· Night resolution: 700TVLs

· Wide dynamic range performance with ON/OFF control

· Sense up 520X and ELC

· Camera ID

· Remote control with extra apparatus

· XDR (eXtended Dynamic Range)

· Motion detection

· C/Cs mount

· Minimum illumination: (0.0002Lux @ F1.2 15IRE),

(0.00008Lux @ 50IRE) all with sense up ON

· S/N Ratio: more than 50dB

· Built in operational OSD

· 1EA alarm output

· 8 privacy zone masking at polygonal method

· 3D motion adoptive DNR

· VPS (Virtual Progressive Scan)

· Synchronization system: internal and external

· 1/4” Sony super HAD CCD sensor

· Super high resolution 600TVLs in color mode, 700TVLs

B/W resolution

· WDR performance with ON / OFF control

· Sense up 520X and ELC

· Camera ID on 255 selectable for zoom control.

· Remote control through RS-485, multiple protocols

(Pelco D & P)

· SSNR ON/OFF

· Minimum focus distance 1m

· 37X optical zoom, f=3.5~129.5mm, F=1.6~3.9

· Minimum illumination: (0.5Lux @ F1.6 normal color

mode), (0.00004Lux @ 50IRE) all with sense up ON

· S/N Ratio: more than 50dB

· Built in operational OSD

· BLC/HLC

· White balance: ATW / outdoor / AWC / manual

· 3D motion adoptive DNR

· 8 privacy zone masking

· Synchronization system: internal

MZ-INBH-5604                       MZ-INBH-3334                       MZ-OBH-5542

Indoor Box Camera

· 1/3” Sony super HAD IT CCD sensor, All in 1 DSP

· Total pixels: 440kP PAL

· Resolution: more than 600TVLs

· Lens mount C/Cs Mount

· Minimum Illumination: 0.12Lux (15IRE)

· Video output VBS 1.0Vp-p composite / 75Ω

· S/N ratio: more than 50dB (AGC OFF)

· White balance: auto

· External controls DC lens level control

· Shutter speed 1/60 ~1/120,000sec NTSC,

1/50~1/100,000sec PAL

· OSD, DNR, BLC, D&N, AGC, CAMERA ID

· 8 Privacy zones masking based on polygonal method

· Wide dynamic range

· RS-485 multi-protocol serial communication port

· Sense up for extremely low light shooting

· Dual power supply

· Synchronization system: internal

Indoor box camera

· 1/3” Sony super HAD IT CCD II sensor

· Total pixels 270K NTSC , 320K PAL

· Resolution: 330TVLs

· Lens mount C/Cs

· Minimum illumination: 0.005Lux @ F0.8

· S/N ratio: more than 50dB (AGC OFF)

· White balance: auto

· External DC lens level control

· AGC ON/OFF

· ELC ON/OFF

· Shutter speed 1/60~1/100,000sec NTSC,

1/50~1/100,000sec PAL

· Gamma correction 0.45

· VBS 1.0V.p.p. composite / 75

· OSD menu driven

· Synchronization system: internal

w w w . m e z o r y . c o m

Outdoor IR Weatherproof Bullet Bi-Camera

· 1/3” Sony super HAD IT dual CCD sensor

· Total pixels 811(h) x 508(v) NTSC, 795(h) x 596(v) PAL

· Resolution: 540TVLs

· IR LED 60 pcs

· Lens (day): F-Stop = 2.0, f = 4mm, 12mm, 16mm options

· Lens (night): F-Stop = 1.8, f = 4mm, 12mm, 16mm op-

tions

· Weatherproof IP66

· IR built-in illumination distance 30m

· Mini illumination: under 0.000lux for infrared lighting

condition

· White balance: auto

· Shutter speed 1/60 ~ 1/100,000sec 1/50~1/100,000sec

· Gamma correction r=0.45

· 2:1 interlaced 625 VTVLs

· BLC

· DC fan included

· Synchronization system: internal

M I S S I O N  O F  S A F E T Y

MZ-VNVDH-4554                      MZ-IRDH-4544                       MZ-DS-4564

Vandal Proof Outdoor Fixed Dome Camera              Indoor IR Fixed Dome Camera                        Indoor Super CMOS Fixed Dome Camera

· 1/3” Sony super HAD II IT CCD sensor

· Effective pixels: 768(H) x 494(V) NTSC, 752(H) x 582(V)

PAL

· Resolution: 550 TVLs

· NCS DSP chipset

· Lens: DC auto iris varifocal lens 4~9 mm

· Minimum illumination: 0.1 Lux at F1.2 (50IRE, AGC ON)

· Video output: 1.0V.p.p. composite video at 75ohm

· Scanning system 2:1 Interlaced

· S/N ratio: more than 50dB

· Electronic shutter 1/60sec ~ 1/120,000sec NTSC;

1/50sec ~ 1/100,000sec PAL (~1/120,000 FL)

· Backlight compensation (BLC)

· Fixed white balance

· IP65 weatherproof certified

· Vandal and weather Proof IP67

· 1/3” Sony super HAD CCD sensor

· Total pixels: 811 (H) x 508 (V) NTSC, 795 (H) x 596 (V)

PAL

· Effective pixels: 768 (H) x 494 (V) NTSC, 752 (H) x 582

(V) PAL

· Day resolution: more than 540 TVLs

· Night resolution: more than 600 TVLs

· IR LED 10pcs (850nm)

· Lens: fixed board lens f4mm @ F = 1.8

· Minimum illumination: 0.1 Lux at color mode; 0 Lux for

infrared lighting condition

· Night vision distance: 10m

· S/N ratio: more than 50dB

· Shutter speed 1/60 ~ 1/100,000 sec 1/50 ~ 1/100,000sec

· White balance: auto (AWB)

· Composite video signal at 1V.p.p., 75ohm

· 1/3” super CMOS sensor

· Effective pixels: 768 (h) x 494 (v) NTSC, 752 (h) x 582

(v) PAL

· Resolution: 560 TVLs

· Lens: fixed board 3.6mm

· Minimum illumination: 0.5 Lux

· S/N ratio: more than 50dB @ AGC OFF

· Shutter speed 1/60 ~ 1/100,000sec NTSC, 1/50 ~

1/100,000sec PAL

· White balance: AWB ( 2,100˚k ~ 9,100˚k)

· Gamma correction r = 0.45

· AGC: max 4 ~ 30 dB

· Composite video signal at 1V.p.p., 75ohm

· Low power consumption for only 50mA at 12VDC

· Audio S/N ration: more than 35dB

· Synchronization system: internal

· Gamma correction r=0.45

· Flickerless and AGC selectable ON/OFF

· Wall, pendant and ceiling mount brackets(optional)

· Synchronization system: internal

MZ-OVBH-7602                      MZ-OBH-4552                       MZ-OBC-4422

Outdoor IR Weatherproof Box Camera

· 1/3 Sony super HAD CCD applied sensor

· SS.A1 DSP chipset

· Day resolution: 600TVLs

· Night resolution: 700TVLs

· Auto white balance

· IR LED 65 pcs of 850nm,

· Night vision distance 100m

· Built-in DC Iris f=6~50mm Vari-focal Lens

· Wide Dynamic Range

· Minimum illumination: 0.12Lux in day, 0.0001Lux with

ICR, 0.00004Lux

· S/N ratio: 52dB

· Weather proof IP66

· Built-in blower function for varying temperature

· Video output VBS 1.0Vp-p composite / 75Ω

· BNC connector

· Sunshade

Outdoor IR LED Bullet Camera

· 1/3” Sony super HAD CCD Sensor

· Effective pixels: 768(H) x 494(V) NTSC, 752(H) x 582(V)

PAL

· Resolution: 550 TVLs

· IR LED 24 pcs

· Lens: Fixed Lens 4.3mm

· Weatherproof IP66

· Night vision distance 30m

· Minimum illumination: 0.1Lux @ F1.2 (CDS Sensor on

0.00 Lux)

· S/N ratio: more than 45dB

· Scanning system 2:1 Interlaced

· Electronic shutter 1/60sec ~ 1/120,000sec NTSC,

1/50sec ~ 1/120,000sec PAL

· Video output: 1 V.p.p. composite / 75Ohm

· BNC connector

· Synchronization system: internal

w w w . m e z o r y . c o m

Outdoor IR LED Bullet Camera

· 1/3” new IT CCD Sensor

· Effective pixels: 510(H) x 492(V) NTSC, 500(H) x 582(V)

PAL

· Resolution: 420 TVLs

· IR LED 24 pcs

· Lens: Fixed Lens 4.3mm

· Weatherproof IP66

· Night vision distance 30m

· Minimum illumination: 0.1Lux @ F1.2 (CDS Sensor on

0.00 Lux)

· S/N ratio: more than 45dB

· Scanning system: 2:1 Interlaced

· Electronic shutter 1/60sec ~ 1/120,000sec NTSC,

1/50sec ~ 1/120,000sec PAL

· Video output: 1 V.p.p. composite / 75Ohm

· BNC connector

· Synchronization system: internal

M I S S I O N  O F  S A F E T Y

MEZORY

MZ-OVNHZ

37-10552

MEZORY Outdoor IR LED Bazooka 37X Zoom Camera MZ-OVNHZ37-10552

· 1/4” Sony super HAD Color CCD

· Built-in 37X auto focus optical zoom, f=3.5mm(F1.6) ~ f=129.5mm(F3.9)

· Digital 12X, minimum focus distance 1’500mm

· Day resolution: 550TVLs, Night resolution: 680TVLs

· True day / night (ICR), DSS, SSNR

· Main IR LEDs ( 10ф x 12ea)

· Sub1/2 IR LEDs ( 10ф x 24ea) & high power IR chip LEDs: 8ea

· IR visible range: max. 150m, 0 lux moonless night (IR LED on)

· Auto dimming control according to zoom ratio

MZ-OVNHZ10-9552

Outdoor IR LED Bazooka 10X Zoom Camera

· Built- in OSD, RS-485 (2400/9600/38400 bps), control protocols (Pelco D /

Pelco P / STD / AD / Honeywell / DynaColor)

· Cable managed bracket, second video output

· Waterproof IP67

· WDR (optional), ATW, AWC, camera ID 255 char, OSD with ID and zoom ratio

· AC 24V / DC 12V dual voltage

· Built-in heater & fan

· Privacy: 8 zones

· Alarm: 4 input, 1 output

· 1/4” Sony super HAD Color CCD

· Built-in 10X auto focus optical zoom,

f=3.8mm(F1.6) ~ f=38mm(F3.9)

· Digital 12X, minimum focus distance

1’500mm

· Day resolution: 550TVLs

· Night resolution: 680TVLs

· True day / night (ICR), DSS, SSNR

· Main IR LEDs ( 10ф x 12ea)

· Sub IR LEDs ( 10ф x 24ea) & high

power IR chip LEDs: 8ea

· IR visible range: max. 150m, 0 lux

· Built- in OSD, RS-485 (2400/9600/38400

bps), control protocols (Pelco D / Pelco

P / STD / AD / Honeywell / DynaColor)

· Cable managed bracket, second video

output

· Waterproof IP67

· WDR (optional), ATW, AWC, camera ID

255 char, OSD with ID and zoom ratio

· AC 24V / DC 12V dual voltage

· Built-in heater & fan

· Privacy: 8 zones

· Alarm: 4 input, 1 output

moonless night (IR LED on)

· Auto dimming control according to zoom

ratio

w w w . m e z o r y . c o

Thnx For Visit Our Webside

Easy Contact Us: +971501521908

Email:Burhanuddin.noorkhanji@gmail.com